This page was exported from Braindump2go Free Latest Microsoft Hot Exam Dumps In PDF & VCE Free Download [    https://www.symantecdumps.com    ]

Export date: Thu Apr 18 17:15:59 2024 / +0000 GMT

## [2017-July-News]Braindump2go NSE4 PDF and NSE4 VCE Instant Download[311-321]

2017/July New NSE4 Exam Dumps with PDF and VCE Free Updated in www.Braindump2go.com  Today!

100% NSE4 Real Exam Questions! 100% NSE4 Exam Pass Guaranteed!

1.|2017 New NSE4 Exam Dumps (PDF & VCE) 360Q&As Download:

https://www.braindump2go.com/nse4.html

2.|2017 New NSE4 Exam Questions & Answers Download:

https://drive.google.com/drive/folders/0B75b5xYLjSSNVi1ISU1vQUxBOTg?usp=sharing

QUESTION 311

View the example routing table. Which route will be selected when trying to reach 10.20.30.254?

A.    10.20.30.0/26 [10/0] via 172.20.168.254, port2

B.    The traffic will be dropped because it cannot be routed.

C.    10.20.30.0/24 [10/0] via 172.20.167.254, port3

D.    0.0.0.0/0 [10/0] via 172.20.121.2, port1

Answer: A

QUESTION 312

When browsing to an internal web server using a web-mode SSL VPN bookmark, which IP address is used as the source of the HTTP request?

A.    The FortiGate unit's public IP address

B.    The FortiGate unit's internal IP address

C.    The remote user's virtual IP address

D.    The remote user's public IP address

Answer: B

QUESTION 313

What is FortiGate's behavior when local disk logging is disabled?

A.    Only real-time logs appear on the FortiGate dashboard.

B.    No logs are generated.

C.    Alert emails are disabled.

D.    Remote logging is automatically enabled.

Answer: A

QUESTION 314

What traffic and attacks can be blocked by a web application firewall (WAF) profile? (Choose three.)

A.    Traffic to inappropriate web sites

B.    SQL injection attacks

C.    Server information disclosure attacks

D.    Credit card data leaks

E.    Traffic to botnet command and control (C&C) servers

Answer: BCE

QUESTION 315

Which statements about One-to-One IP pool are true? (Choose two.)

A.    It allows configuration of ARP replies.

B.    It allows fixed mapping of an internal address range to an external address range.

C.    It is used for destination NAT.

D.    It does not use port address translation.

Answer: BC

QUESTION 316

Which statements correctly describe transparent mode operation? (Choose three.)

A.    All interfaces of the transparent mode FortiGate device must be on different IP subnets.

B.    The transparent FortiGate is visible to network hosts in an IP traceroute.

C.    It permits inline traffic inspection and firewalling without changing the IP scheme of the network.

D.    Ethernet packets are forwarded based on destination MAC addresses, not IP addresses.

E.    The FortiGate acts as transparent bridge and forwards traffic at Layer-2.

Answer: CDE

QUESTION 317

View the exhibit. What is the effect of the Disconnect Cluster Member operation as shown in the exhibit? (Choose two.)

A.    The HA mode changes to standalone.

B.    The firewall policies are deleted on the disconnected member.

C.    The system hostname is set to the FortiGate serial number.

D.    The port3 is configured with an IP address for management access.

Answer: AD

QUESTION 318

What step is required an SSL VPN to access to an internal server using port forward mode?

A.    Configure the virtual IP addresses to be assigned to the SSL VPN users.

B.    Install FortiClient SSL VPN client

C.    Create a SSL VPN realm reserved for clients using port forward mode.

D.    Configure the client application to forward IP traffic to a Java applet proxy.

Answer: D

QUESTION 319

View the exhibit. This is a sniffer output of a telnet connection request from 172.20.120.186 to the port1 interface of FGT1.

In this scenario. FGT1 has the following routing table:

Assuming telnet service is enabled for port1, which of the following statements correctly describes why FGT1 is not responding?

A.    The port1 cable is disconnected.

B.    The connection is dropped due to reverse path forwarding check.

C.    The connection is denied due to forward policy check.

D.    FGT1's port1 interface is administratively down.

Answer: B

QUESTION 320

An administrator needs to be able to view logs for application usage on your network. What configurations are required to ensure that FortiGate generates logs for application usage activity? (Choose two.)

A.    Enable a web filtering profile on the firewall policy.

B.    Create an application control policy.

C.    Enable logging on the firewall policy.

D.    Enable an application control security profile on the firewall policy.

Answer: BD

QUESTION 321

A company needs to provide SSL VPN access to two user groups. The company also needs to display different welcome messages on the SSL VPN login screen for both user groups.

What is required in the SSL VPN configuration to meet these requirements?

A.    Two separated SSL VPNs in different interfaces of the same VDOM

B.    Different SSL VPN realms for each group

C.    Different virtual SSLVPN IP addresses for each group

D.    Two firewall policies with different captive portals

Answer: D

!!!RECOMMEND!!!

1.|2017 New NSE4 Exam Dumps (PDF & VCE) 360Q&As Download:

https://www.braindump2go.com/nse4.html

2.|2017 New NSE4 Study Gudie Video:

YouTube Video: YouTube.com/watch?v=lcPSEfJYR0M

Post date: 2017-07-18 09:53:02

Post date GMT: 2017-07-18 09:53:02

Post modified date: 2017-07-18 09:53:02

Post modified date GMT: 2017-07-18 09:53:02

Powered by [ Universal Post Manager ] plugin. MS Word saving format developed by gVectors Team    www.gVectors.com